## Slide 1
GROUP 5
Needle-free
Immunization
Wanghan Sun, Ruslan Shupanov,
Xinya Zheng, Ling Ji, Edward Small
1

## Slide 2
Wanghan Sun
1
INTRODUCTION
2

## Slide 3
Background
PROBLEM
What is the final depth of the particles being blown into the skin?
Main purpose
Analyze the behavior of the particles as they move through the cortex and to calculate how deep in the cortex the particles will end up resting.
3

## Slide 4
Ling Ji
2
PHYSICAL
MODEL
4

## Slide 5
  The motion of the particles
  In the skin
Stratum corneum (SC)
Viable epidermis (VE)
Langerhans cell (LC)
Gold particle
is the density of the skin
(treated as a fluid with constant properties)
is the cross-sectional area of the particle
is its velocity
is an empirical drag coefficient
yield stress of the material.
C yield constant
THE STRUCTURE
SC
VE
5

## Slide 6
Relevant parameters to be used in the model
 | Value | Remark
Drag coefficient | ~0.5 | 
Gold particle radius [2] | 0.5-2.5 | Normal distribution (1.5, 0.5)
Particle velocity on entry | 400-600 | Normal distribution (500, 51)
Yield stress of SC[3] | 3-25 | Normal distribution (14, 6)
Yield stress of VE | 2 | 
Density of SC | 1500 | 
Density of VE | 1200 | 
Thickness of SC[1] | 20-30 | Normal distribution (25, 2.6)
Thickness of VE[1] | 50-100 | Normal distribution (75, 13)
Yield constant c | ~3 | 
 | Value | Remark
 | ~0.5 | 
 |  | Normal distribution (1.5, 0.5)
 |  | Normal distribution (500, 51)
 |  | Normal distribution (14, 6)
Thickness of SC[1] |  | Normal distribution (25, 2.6)
Thickness of VE[1] |  | Normal distribution (75, 13)
Yield constant c | ~3 | 
*see reference
6

## Slide 7
Ruslan Shupanov
3
ANALYTICAL
SOLUTION
7

## Slide 8
8

## Slide 9
9

## Slide 10
10

## Slide 11
  Some results
11

## Slide 12
Edward Small
4
NUMERICAL
SOLUTION
12

## Slide 13
Algorithm
13

## Slide 14
  Numerical results using distribution table
2
1
27.17% of cells end in the LC layer or go beyond it.
Most particles fall short
14

## Slide 15
  The effectiveness of the method
Viable area to consider an LC cell "hit" is
π(R + 2×R1)^2 = 0.000154mm^2
1000 LC cells per mm^2, so 15.4% of the area is considered "successful hit".
Assumption
The LCs have a radius R = 4um and particles have a radius R1 = 1.5um (the mean).
A gold particle that has landed in the LC layer has an equal probability of landing anywhere in the LC layer.
Hitting an LC does not remove it from the system
R
R1
15

## Slide 16
Each particle has a 84.6% chance of missing.
For half the particles to have a 95% chance of being hit, we require
0.846^(n/2) = 0.05
n/2= 17.91, so require approximately n=8.955 particles per LC cell to land in the LC zone.
Need 8955 particles in LC zone. With a 27.17% rate of landing in the zone, we require approximately 32959 particles to be fired
What Can we change?
  Under the assumption, do some calculations:
16

## Slide 17
Increasing initial velocity
Changing mean particle radius and standard deviation
Changing radius mean and SD would reduce particles needed from 32959 to approximately 14663, so only need 44.49% of particles
Depth in the skin where a particle comes to rest(V0
Good=41.39%
Depth in the skin where a particle comes to rest(
Good=61.07%
17

## Slide 18
Xinya Zheng
5
EXPANSION ON
THE MODEL
18

## Slide 19
Problems in our model
We don’t consider the fluid dynamics
The diffusion of particles through the skin is not taken into account
We assume the particles don’t break up in anyway
We don’t consider too much of biological modelling
Probability calculation needs to be refined more accurate
Hitting an LC does not remove it from the system( several particles will hit the same LC)
Particles and cells are three-dimensional, and the two-dimensional model has its limitations
A simple thought of the improvement of the model
19

## Slide 20
3-D model
The initial position（x0,y0,z0）
The random radius r0
The random velocity v0
The initial number of particles N0
These particles have random radius and velocity (and other quantities, like position)
Use the two-layers model to calculate x(t)(final depth)
The finial position（x0,y0,z0+X（t））
The finial number of particles N
（we can use the position value to see how these particles distributed in the LC layer, generally.)
20

## Slide 21
In the small space around the one Langerhans cell, if the concentration of particles exceeds a certain value, the Langerhans cell can be considered to have been hit successfully (Successful absorption).
From some research, we suppose that “LCs form a monolayer network of cells distributed evenly throughout the suprabasal layers of the epidermis”
(*see reference [4])
Assumption
Hypothesis
Uniform distribution
(Then we can also have the position of the LCs)
In the 2D model, the particles need to reach the depth of the Langerhans cell to hit the cell correctly, while in the 3D model, the concentration of the particles in the space around the Langerhans cell is used as a parameter for probability calculation.
21

## Slide 22
Reference
[1]Egawa, M. et al.(2007) ‘In vivo Estimation of Stratum Corneum Thickness from Water Concentration Profiles Obtained with Raman Spectroscopy’,Actadermato-venereologica87, pp. 4–8.
[2]He, L. et al.(2013) ‘Statistics of multiple-scatterer induced frequency split-ting in whispering gallery microresonators and microlasers’,New Journal ofPhysics15
[3]Maria, F. L. et al.(2015) ‘A mechanistic insight into the mechanical role of the stratum corneum during stretching and compression of the skin’,Journal of the Mechanical Behavior of Biomedical Materials49, pp. 197–219
[4]YU, R., ABRAMS, D., ALAIBAC, M. and CHU, A. (1994), Morphological and quantitative analyses of normal epidermal Langerhans cells using confocal scanning laser microscopy. British Journal of Dermatology, 131: 843-848.
https://github.com/Teddyzander/transferable_skills/
Code link
22

## Slide 23
THANK YOU FOR LISTENING!
ANY QUESTIONS?
23